## Slide 1: Biblioteca 1-Wire para sAPI Proyecto CIAA Protocolos de Comunicación en Sistemas Embebidos Carrera de Especialización de Sistemas Embebidos
Autor: Ing. Mauro Moreyra
Agosto 2018

## Slide 2: Protocolo 1-Wire Conceptos básicos
Diseñado por Dallas Semiconductor (±1988), hoy parte de Maxim Integrated (2001).
Provee transferencia de datos a baja velocidad (estándar hasta 15.4 Kbps, overdrive hasta 125 Kbps) y energía (power) sobre un único cable + GND.
Comunicación half-duplex (bidireccional).
No requiere clock: el bus se sincroniza con los flancos negativos de los pulsos del master.
Opera con niveles CMOS/TTL.

## Slide 3
MAESTRO
ESCLAVOS MicroLan™
2k2 ✓
“LASERED ROM”
Protocolo 1-Wire Esquemático bus
Notes: 64-Bit ID se comporta como una MAC ADDRESS, código único e irrepetible entre todos los dispositivos 1-Wire.

## Slide 4
Lineal
Estrella
Stubbed
Protocolo 1-Wire Topologías de red
Notes: Es a modo ilustrativo… tener en cuenta que en topologías complejas (estrella o redes switcheadas), aparecen otros factores a considerar: impedancia distribuida, problemas con las fuentes parásitas distribuidas, los tiempos de propagación según el largo de los cables, etc.

## Slide 5
Pulso de reset (Master) y pulso de presencia (Esclavo).
Protocolo 1-Wire Señalización
Notes: Hay 4 operaciones atómicas básicas con las que se construyen las comunicaciones mediante 1-Wire.
1-Wire communication begins with a reset-/presence-detect cycle (Figure 1). To get from idle to active, the voltage on the 1-Wire bus must fall from VPUPbelow the threshold, VTL. To get from active to idle, the voltage needs to rise from VILMAX past the threshold, VTH. The time it takes for the voltage to make this rise is seen in Figure 1 as "ε," and its duration depends both on the pullup resistor, RPUP, used and the capacitance of the 1-Wire network attached. The voltage VILMAX is relevant for the slave when determining a logical level, not for triggering any events. If the master uses slew-rate control on the falling edge, the master must pull down the line for tRSTL + tF to compensate for the edge. A tRSTL duration of 480µs or longer exits the Overdrive Mode, returning the device to standard speed. If a slave is in Overdrive Mode and tRSTL is no longer than 80µs, the device remains in Overdrive Mode. If a slave is in Overdrive Mode and tRSTL is between 80µs and 480µs, the device will reset but the communication speed is undetermined. After the bus master has released the line, it goes into receive mode. Now the 1-Wire bus is pulled to VPUP through the pullup resistor. When the threshold, VTH, is crossed, the slave waits for tPDH and then transmits a presence pulse by pulling the line low for tPDL. To detect a presence pulse, the master must test the logical state of the 1-Wire line at tMSP. The tRSTH window must be at least the sum of tPDHMAX, tPDLMAX, and tRECMIN. Immediately after tRSTH is expired, a slave with the new front-end is ready for data communication.
Read/Write Time Slots
After the reset-/presence-detect cycle is completed, a 1-Wire slave is ready for communication using time slots. Each time slot carries a single bit. Write time slots transport data from the bus master to a slave. Read time slots transfer data from a slave to the master. Figure 2 illustrates the definitions of the write and read time slots. A time slot begins with the master pulling the data line low. As the voltage on the 1-Wire line falls below the threshold, VTL, a slave starts its internal timing generator, which determines when the data line is sampled during a write time slot and how long data is valid during a read time slot.

## Slide 6
Write-One time slot.
Protocolo 1-Wire Señalización
Notes: Master-to-Slave
For a write-one time slot, the voltage on the data line must have crossed the VTH threshold before the write-one low time, tW1LMAX, is expired. For a write-zero time slot, the voltage on the data line must stay below the VTH threshold until the write-zero low time, tW0LMIN, is expired. After the VTH threshold has been crossed, a slave needs a recovery time, tREC, before it is ready for the next time slot.

## Slide 7
Write-Zero time slot.
Protocolo 1-Wire Señalización

## Slide 8
Read-Data time slot.
Protocolo 1-Wire Señalización
Notes: Slave-to-Master
A read-data time slot begins like a write-one time slot. The voltage on the data line must remain below VTL until the read-low time, tRL, is expired. During the tRL window, when responding with a 0, a slave starts pulling the data line low; its internal timing generator determines when this pulldown ends and the voltage starts rising again. When responding with a 1, a slave does not hold the data line low, and the voltage starts rising as soon as tRL is over. The sum of tRL + δ (rise time) on one side and the internal timing generator of the slave on the other side define the master sampling window, tMSRMIN to tMSRMAX, in which the master must perform a read from the data line. After reading from the data line, the master must wait until tSLOT is expired.

## Slide 9
Protocolo 1-Wire Comandos ROM
Comando | Código | Descripción
Read ROM | 0x33 | Leer 64-bit ID (un esclavo)
Skip ROM | 0xCC | Direccionar todos los esclavos conectados al bus
Match ROM | 0x55 | Direccionar función a un único esclavo conectado al bu
Search ROM | 0xF0 | Descubrir el ID de todos los esclavos conectados al bus
Otros comandos: Read scratch; Write scratch; Read status; Write status; etc. |  | 

## Slide 10
Protocolo 1-Wire Comunicación en tres fases
(OPTIONAL)
Notes: 8-BIT ROM FUNCTION Command Code (Unique device is selected): este envio de comando corresponde únicamente en caso de que querramos seleccionar un único esclavo dentro del bus 1-Wire (obviamente no aplica para buses con un único esclavo).

## Slide 11
Protocolo 1-Wire Dispositivos 1-Wire: iButtons
Identification only
Identification plus control
Identification plus temperature
Identification plus time (RTC)
Identification plus NV SRAM
Identification plus OTP EPROM
Identification plus EEPROM
Identification plus SHA-1 secure EEPROM
Identification plus logging
Notes: 1-Wire devices are offered in conventional transistor (TO-92) and IC packages (TSOC, SOIC, SOT23). Designed for contact applications and easy attachment, the 2-contact SFN1 package accommodates parasitically powered 1-Wire devices (Figure 2). The 16mm-diameter stainless steel iButton®2 package protects 1-Wire devices from harsh environments, making them suitable for indoor and out door use (Figure 3). Many devices are also available in flip chip (Figure 4) and UCSP™3 (Figure 5) versions.

## Slide 12
Estrategia: Bit-Banging por SW + delay bloqueantes.
Funciones públicas básicas (ROM).
Funciones privadas para añadir soporte a más comandos y dispositivos.
6us
64us
60us
10us
9us
55us
0us
480us
70us
410us
@ STANDARD SPEED
Biblioteca 1-Wire sAPI Características

## Slide 13
Secuencia para consulta de datos de ROM.
Biblioteca 1-Wire sAPI Testing: Medición con analizador lógico

## Slide 14
Biblioteca 1-Wire sAPI Demo

## Slide 15
Repositorio sAPI 1-Wire https://github.com/MauroMoreyra/sapi_oneWire
1-Wire Overview https://www.maximintegrated.com/en/products/1-wire/flash/overview/
1-Wire Communication Through Software https://www.maximintegrated.com/en/app-notes/index.mvp/id/126#
Reading and Writing 1-Wire® Devices Through Serial Interfaces https://www.maximintegrated.com/en/app-notes/index.mvp/id/74
Overview of 1-Wire Technology and Its Use https://www.maximintegrated.com/en/app-notes/index.mvp/id/1796
Complete 1-Wire command codes http://owfs.sourceforge.net/family.html
Guidelines for Reliable Long Line 1-Wire Networks https://www.maximintegrated.com/en/app-notes/index.mvp/id/148
Repositorio GitHub y Bibliografía

## Slide 16: ¿Preguntas?

## Slide 17: ¡Muchas gracias!